# Soy Candle Kit Instructions

Kit contents:

EcoSoya CB-135 Soy Wax: 3 lbs.
Zinc Core Wicks: 12 pcs.
Candle Containers: 12 votive containers x 3 oz. glass
Thermometer
Fragrance Oils:  6 bottles x 1 oz. ULTRA CONCENTRATES (enter names in box below)
Small Eyedroppers: 6 pcs. (for mixing your blends)
Scent Strips: 10 pcs.(for sampling your fragrance creations)
Instruction Sheets & Labels
Gloves: 3 pcs.
D&C Colorant: Red & Blue 3/16 dram (oil based)

Before you begin, please note that all of your materials and workspace need to be made of HDPE plastic, stone, metal, glass or wood (no acrylics, vinyl or varnished tabletops etc., no PVC or low density plastics).  The oils are made of compounds that can disintegrate certain plastics and varnishes.  Gloves are provided for use to keep hands safe from any irritation.

| Step 1) | Create your fragrance. You can use the fragrances you purchased as they are, but you are also provided with all you need to mix your own blends. Using a scent strip, place drop(s) of oil you wish to use as a base. Then add others by drops as well on the strip. Let it dry down and then smell – adjust accordingly by adding other fragrances as desired. Jot down your formulas in drops and then make your batch using those ratios multiplied out the desired quantity. |
| --- | --- |
| Step 2) | Melt your wax. In a small pot over low flame, melt soy wax until liquefied. Alternatively, if you have one, set your electric wax & butter melter to 120° F and allow wax to melt. Watch your wax carefully to avoid burning because once it is burned, you will not be able to rescue your burnt smelling wax. |
| Step 3) | Wick your containers. While the wax is melting, carefully dip the flat metal tabbed portion of your wick into the liquid portion of the wax. Center and press the wax coated wick tab into the bottoms of your 3 oz votive style container, making sure that the wick stands upright. Repeat for all containers you wish to fill. |
| Step 4) | Add fragrance to your wax. Pour desired amount of wax into a measuring cup or pouring vessel. Use the provided thermometer to verify the current temperature. Once the temperature of the wax has cooled to 120° F, blend in your selected fragrance at a rate of 6-9% of the overall wax mixture. For simplicity, 8% or 1 1/2 tsp. of fragrance per 3 oz. candle is sufficient (multiply up for more than 1 candle). Stir thoroughly until evenly mixed. For 1 lb. batches, we suggest adding 1 1/2 oz. (3 tbsp.) fragrance for 1 lb. of wax and then pouring – for 1/2 lb. batches, then divide by two. |
| Step 5) | Color your candle wax. For color, use the wand that is included with your vial. Dip the colored wand into your candle base mixture and swirl. Wipe wand and repeat, dipping into the dye and then into the mixture until desired color is met. Stir complete until color is uniform. |
| Step 6) | Pour your candles. Quickly pour your scented wax into your pre-wicked votive style containers, allowing 1/2 inch of clearance between the rim and the top of the wax. Be sure to do this soon after adding the fragrance and mixing -- you do not want your fragrance to burn off. Allow candles to cool. Trim wicks to 1/4 inch. |
| Step 7) | Label your candles Label each candle with the provided labels. Be sure to include round warning label stickers on the bottom of each candle. |

That’s it! Your candles are ready for personal use, or to be given to your friends as gifts, or even sold for a nice little profit. Remember to trim your wick every 30 minutes for optimum burn and to avoid carbon build up!